## Slide 1: Monthly Meeting
Aug 2024

## Slide 2: Agenda
    Background Knowledge
    Exploration of LiDAR enhanced CL Control of Helix
    To do (Roadmap)

## Slide 3: LiDAR-Enhanced Closed Loop Wake Mixing Control
Aug 2024

## Slide 4: Wake Effect
Effect on downstream WT:
Less power production
Increase structural loads
20 – 45% Loss of Energy
Notes: The downstream turbine encounters a significantly reduced free-stream velocity compared to the upstream turbine, leading to less energy being available in the flow.

## Slide 5: Wind Farm Flow Control
    Axial Induction Control
    Wake Steering
    Wake Mixing

## Slide 6: Axial Induction Control
Derate
the potential for increased energy extraction is rather low
Normal Operation
Axial Induction Control
Notes: Delibrately operate the upstream turbine below the maximum condition to save more energy to the downstream turbine

## Slide 7: Wake Steering
Notes: Decrease the overlap between the upstream turbine’s wake and the downstream turbine’s air by a yaw offset.
Advanced for commercial usage
Challenges remain in this area mostly related to the complex response of the wake to yaw set-points and its strong dependence on atmospheric conditions.

## Slide 8
Notes: Decrease the overlap between the upstream turbine’s wake and the downstream turbine’s air

## Slide 9: Wake Mixing
Notes: This slide shows how the wake evolves with increasing distance from the turbine.
Wake recovers by mixing with the free-ambient air. Thus, if we can facilitate this mixing, there will be a faster recovery of wake, and thus, increase the power generation of the downstream turbine.
So let’s delve a bit deeper into how the wake is mixed.

## Slide 10: Wake Mixing
Notes: Two mechanisms:
Tip & Root Vortex breakup
Wake Meandering
These two facilitate the mixing of wake with the ambient air. Hence, the wake mixing technique aims to facilitate those two things deliberately

## Slide 11: Wake Mixing
Facilitate mixing of free-ambient air and wake for wake recovery
Notes: The arrow stands for the thrust force

## Slide 12: Wake Mixing
Facilitate mixing of free-ambient air and wake for wake recovery
Notes: The wake mixing control strategy is developed to enhance the mixing of the turbine’s wake with ambient free-stream velocity air. This enhanced mixing accelerates the energy recovery of the wake more effectively than would occur through natural wake processes and recovery mechanisms.
Pulse: varying thrust coefficient sinusoidal ----> Load ----> More consistent
Helix: Individual Pitch Control

## Slide 13: Helix --- MBC Transform
Rotating Frame  Non-rotating Frame
Notes: MBC transform map the signals from rotating frame to the non-rotating one.
In this fixed frame, the individual pitch commands can be computed as decoupled collective, tilt, and yaw pitch commands respectively, allowing simple SISO control loops instead of MIMO

## Slide 14: Helix --- Inverse MBC Transform
Non-rotating Frame  Rotating Frame
Notes: By using the inverse MBC, we just need to give the tilt and yaw moment, then the blade pitch signals are acquired.

## Slide 15: Helix --- Block Diagram
Sinusoidal signals
Frequency
Amplitude
Phase
Notes: Beta(tilt) and Beta(yaw) for rotor disk, based on the phase different of tilt and yaw, the helix is clockwise or counterclockwise

## Slide 16: Gap of the Helix
Open-Loop Control:
No feedback from output
Can we closed-loop control the helix approach based on flow information?
Notes: Disturbance Rejection
Accuracy and Precision
Input-based control vs. Output-based control: Directly monitors and adjusts the system outputs.

## Slide 17: Research Question
    How to closed-loop control the helix approach?
    Handle model error, uncertainties
    Real-time Control
Notes: The main question, answer WHY you want to do all the stuff?

## Slide 18: Feedback --- LiDAR
Notes: To close the loop, one of the most important things is to get the feedback --- LiDAR

## Slide 20: LiDAR Model
Notes: LiDAR is placed in the perfect location --- 1.86D for IEA15MW so that the diameter of the ring is the same as D

## Slide 21: Research Question
    How to integrate LiDAR and the helix approach for closed-loop wake mixing control for wind farms?
    Which LiDAR configuration to use?
    What feature in the helix wake should be controlled, and how to obtain it using LiDAR?
    How to design the control loop to rectify the helix?
    Potential for next step?

## Slide 24: LiDAR Choosing
    Trade off between practicality and quality --- Modified ZX-TM LiDAR
    Continuous Wave LiDAR (one focal distance)
    10 – 720 m
    Half-cone angle: -
    Entire rotor disk

## Slide 25: Research Question
    How to integrate LiDAR and the helix approach for closed-loop wake mixing control for wind farms?
    Which LiDAR configuration to use? √
    What feature in the helix wake should be controlled, and how to obtain it using LiDAR?
    How to design the control loop to rectify the helix?
    Potential for next step?
Notes: So here, we answered the first question, what configuration of LiDAR to be used.

## Slide 26: Practical Tool
Notes: Q-blade
MATLAB
NREL5MW

## Slide 27: Simulation Setup
1D
1D
Notes: Downwind facing LIDAR
Measuring 1D (rotor disk) position

## Slide 28: Demo of LiDAR
U = 10 m/s
CCW
Str = 0.3
Amplitude = 3
Notes: Q-blade doesn’t have any LiDAR functionality, so I spent around a week time to implement the LiDAR functionality and optimize it so that it’s fast enough (2 days --> 10 mins --> 2 mins )
Wake center is what I am aiming at
1. obvious
2. accessible in real-time

## Slide 29: Why closed-loop control?
Notes: With LiDAR, we are able to visualize the helix downwind, and based on some play arounds, we can answer the question of what to control

## Slide 30: Why closed-loop control?
Notes: With LiDAR, we are able to visualize the helix downwind, and based on some play arounds, we can answer the question of what to control

## Slide 31: What to control?
Notes: CCW, coordinate of helix center, two periodic signal

## Slide 32: MBC Transform
Rotating Frame  Non-Rotating Frame
1P, 1P+fe  0P, fe

## Slide 33: New Transform
Non-Rotating Frame  Helix Frame
1P, 1P+fe  0P, fe
1P, 1P+fe  0P, fe  1P, 0P

## Slide 34: New Transform
Non-Rotating Frame  Helix Frame
1P, 1P+fe  0P, fe
1P, 1P+fe  0P, fe  1P, 0P

## Slide 35: New Transform

## Slide 36: New Transform

## Slide 37: Control Relation Exploration
Principle of Control:
As simple as possible (Static)

## Slide 38: What to control?
Fixed Frame
Helix Frame
FF theta
HF theta
FF center
HF center
Notes: There are four different combination that can be controlled
We explore the relation between input and output by first open-loop control the whole system

## Slide 39: What to control?
Fixed Frame
Helix Frame
HF theta
FF center
HF center
FF theta
Notes: Principle: Simplified as much as possible, so static it is

## Slide 40: What to control?
Fixed Frame
Helix Frame
FF theta
HF theta
FF center
HF center
Notes: There are four different combination that can be controlled
We explore the relation between input and output by first open-loop control the whole system

## Slide 41: FF theta – FF center (Amplitude)
Notes: First the magnitude of beta tilt and beta yaw

## Slide 42: FF theta – FF center (Amplitude)

## Slide 43: FF theta – FF center (Amplitude)

## Slide 44: FF theta – FF center Analysis
Changing magnitude changes rotating magnitude of one degree of freedom
Tilt and Yaw are decoupled and orthogonal
But the rotating nature makes it hard to control

## Slide 45: Center of Center
Notes: With LiDAR, we are able to visualize the helix downwind, and based on some play arounds, we can answer the question of what to control

## Slide 46: FF theta – FF center (Bias)
Notes: And then the bias

## Slide 47: FF theta – FF center (Bias)
Notes: And then the bias

## Slide 48: FF theta – FF center (Bias)
Notes: And then the bias

## Slide 49: FF theta – FF center (Bias)
Notes: And then the bias

## Slide 50: FF theta – FF center (Bias)
Notes: And then the bias

## Slide 51: FF theta – FF center (Bias)
Notes: And then the bias

## Slide 52: FF theta – FF center Analysis
Changing magnitude changes rotating magnitude of one degree of freedom
Tilt and Yaw are decoupled and orthogonal
But the rotating nature makes it hard to control
Very slow process
No free lunch when controlling the center of center

## Slide 53: What to control?
Fixed Frame
Helix Frame
FF theta
HF theta
FF center
HF center
Notes: There are four different combination that can be controlled

## Slide 54: What to control?
Fixed Frame
Helix Frame
FF theta
HF theta
FF center
HF center
Notes: There are four different combination that can be controlled
We explore the relation between input and output by first open-loop control the whole system

## Slide 55: HF theta – HF center
Notes: The magnitude of the helix as well as the phase can both be manipulated

## Slide 56: HF theta – HF center
Notes: First the magnitude of beta tilt and beta yaw

## Slide 57: HF theta – HF center
Notes: First the magnitude of beta tilt and beta yaw

## Slide 58: HF theta – HF center
Notes: First the magnitude of beta tilt and beta yaw

## Slide 59: HF theta – HF center
Notes: First the magnitude of beta tilt and beta yaw

## Slide 60: HF theta – HF center Analysis
Coupling between the (z, y)
MIMO system
Phase and magnitude
Both variables are STATIC!

## Slide 61: FF theta – FF center (Amplitude)

## Slide 62: Research Question
    How to integrate LiDAR and the helix approach for closed-loop wake mixing control for wind farms?
    Which LiDAR configuration to use? √
    What feature in the helix wake should be controlled, and how to obtain it using LiDAR? √
    How to design the control loop to rectify the helix?
    Potential for next step?
Notes: So here, we answered the first question, what configuration of LiDAR to be used.

## Slide 63: Control System Design
LiDAR Sampling Pipeline
Notes: Dead-time Delay

## Slide 64: Dead-time Delay
Notes: Dead-time Delay

## Slide 65: Smith Predictor (CL Yaw Ctrl)
Notes: Equations of internal model and delay.
The internal model predict the reaction of the wake to the demanded yaw angle. The first equation is the relationship of yaw, and then the second one is for the wake.

## Slide 66: Model-based Control

## Slide 67: System IDE --- data processing
Flowchart of LiDAR data processing
Start
Sim Over
LPF
Detrend
Coordinate Transfer
Over
LiDAR sampling
Helix Center Calculation
Y
N

## Slide 68: System IDE
Notes: Dead-time Delay

## Slide 69: System IDE

## Slide 70: System IDE
Rough linearity can be observed
Second-order system
RT = 20s / BW = 0.0175 Hz
MIMO system

## Slide 71: Current Issue

## Slide 72: Current Issue

## Slide 73: Next Step
    System IDE (U = 10m/s)
    Model-based Controller Tuning
    Next step depends on result of 2

## Slide 74: Thanks for listening :)